Lifepak 20 & Lifepak 20e defibrillators

The test plug must remain connected to the therapy cable and the grey plug on the end of the therapy cable is coupled to the test plug. It is only disconnected to connect the defibrillator electrodes

It must remain coupled as the defibrillator is programmed to do an automatic ‘Self test’ daily at 03:00hrs which will generate a print off confirming self test with date & time e.g.

Self test succeeded

19/Aug/2016  03:00

On the daily checklist  the ‘perform defib checks where appropriate’ can be ticked if the print out states ‘Self test succeeded’

If the print out states failed then EBME must be contacted.

The print out must be available as confirmation that the test has been done.

The nurse can sign the print out.

However, when the test has been done the following day the test can be thrown away and the new test results available.

This prevent any unnecessary paper               checks accumulating.

There only needs to be one paper check available.

# Text boxes

The test plug (black) is connected to the therapy cable and must remain so.

DO NOT REMOVE THE TEST PLUG